## Slide 1
MJLAB · DODO
Learning to walk
in simulation first
Policy search for the DODO biped in mjlab — 56 training runs across three task phases, from standing on flat ground to a rough-terrain generator.
AUTHOR
Hera Gishti
PLATFORM
mjlab / rsl_rl (PPO)
ROBOT
DODO biped
RUNS MINED
56 (52 usable)

## Slide 2
01 · INTRODUCTION
Why simulate first
— Start from the DODO URDF — its real kinematic tree, joint limits, and actuator model become the ground truth the simulator has to respect.
— Physics engines are finally good enough — mjlab's MuJoCo backend models contact and actuator dynamics closely enough that policies trained in it are worth trusting.
— And they parallelize — thousands of copies of DODO step together on a GPU, turning what would be sequential hardware trials into one batched search.
— The goal — explore a wide range of candidate control policies for DODO cheaply, in sim, before committing anything to the real robot.
01 / 06

## Slide 3
02 · METHOD
Training pipeline
PPO — held fixed
lr 1e-3 · clip ε 0.2 · γ 0.99 · λ 0.95
adaptive KL 0.01 · 5 epochs · 4 minibatches
actor/critic net [512, 256, 128]
Identical across all 56 runs — never swept.
Terrain curriculum
Flat plane through 2026-06-07
From 06-10: generator terrain — stairs, slopes,
random rough, wave × 10 difficulty rows
terrain_levels advances with success rate
What was actually varied
num_envs: 256 → 1024 → 2048
reward-term weights across 3 phases
(stand → walk → rough)
entropy_coef nudged on 3 of 56 runs
In short: the sweep was over task design and training scale, not PPO hyperparameters — those stayed default the entire time.
02 / 06

## Slide 4
03 · RESULTS — FLAT TERRAIN
Scale mattered more than tuning
03 / 06
Chart: 
| 256 envs | 1024 envs | 2048 envs
Mean reward | 44.6 | 58.5 | 85.6
Mean reward by parallel env count
35 flat-terrain runs (wandb) · r = 0.73 with num_envs
BEST RUN
2026-06-04_23-59-38 · reward 103.4 (peak 105.8)
phase2-adaptive-from-standing-strict-less · 2048 envs — continued next day at reward 103.3
WEAKEST FULLY-LOGGED VARIANT
2026-06-04_22-53-17 · reward 48.3 (peak 54.3)
adaptive-per-env — per-env adaptive scaling underperformed the shared schedule

## Slide 5
03 · RESULTS — ROUGH TERRAIN
Rough terrain: real progress, then a plateau
Run (tag) | Iters logged | Reward pk | Lvl mean pk | Lvl max
06-10_04-22-56 nanfix (best) | 6,491 | 22.1 | 3.5 | 9 / 9
06-10_01-47-04 | 2,800 | 18.1 | 3.5 | 9 / 9
06-14_03-26-33 fixedvel | 339 | 21.7 | 3.5 | 9 / 9
06-18_22-32-58 (1024 envs) | 7,123 | 18.5 | 0.9 | 9 / 9
MAX ≠ TYPICAL
9 / 9
hardest single env, every run
3.5 / 9
population-mean ceiling, 2048-env runs
— Correcting the earlier claim: revised from the wandb-only pass: every 2048-env rough run — regardless of restart, bugfix, or how long it trained — has at least one env clear the entire 9-level curriculum, and the population average consistently tops out around level 3.5. That's a real, reproducible ceiling, not a stall at the easiest tier.
— Best run: 06-10_04-22-56 ("nanfix") trained the longest (6,491 logged iters) with the cleanest termination profile (0% out-of-terrain-bounds) — the best evidence so far that rough terrain is learnable, just not yet past ~level 3.5.
— One outlier: the 1024-env 06-18 run reached the highest final reward (14.9) of any rough run but the lowest terrain-mean ceiling (0.9) — reward and curriculum progress aren't tightly coupled here, likely due to reward-weight revisions between phases.
04 / 06

## Slide 6
04 · CONCLUSION
Where this leaves DODO
WORKING
Flat-ground locomotion is solid
The best runs reach reward ~103-106 once curriculum + reward shaping settle — standing, then walking, then adaptive command tracking, chained across checkpoints.
OPEN PROBLEM
Rough terrain plateaus around level 3.5 of 9
Real, reproducible progress — every 2048-env run clears the hardest single-env tier at least once — but the population average consistently stalls near level 3.5. Longer, uninterrupted training past that ceiling is the open question, not whether it works at all.
NEXT
An actual hyperparameter sweep, then a decomposed critic
PPO's hyperparameters were never really searched — a natural next sweep now that the curriculum is stable. In parallel: a decomposed (HRA-style) critic, one head per reward term, so PPO can credit-assign per objective instead of one scalar.
05 / 06

## Slide 7
APPENDIX · PPO CONFIG
The config held constant across all 56 runs
PARAMETER | VALUE
learning_rate | 1e-3
clip_param | 0.2
gamma | 0.99
lam (GAE) | 0.95
num_learning_epochs | 5
num_mini_batches | 4
desired_kl | 0.01
schedule | adaptive
num_steps_per_env | 24
actor/critic net | [512, 256, 128]
06 / 06